## Slide 1: Project proposed by :
EAST
(Eradication of Accidents using Sensing Technology)
IV –YEAR
Batch no : 13MNCSED-06
A.Surendhar (13881A05L1)
Y.V.S.R.Sampath (13881A05N5)
B.Shravan (13881A05J3)
L.Srikanth (13881A05K8)
Supervised By : S.VenuGopal

## Slide 2
Contents
Objective.
Problem Description.
Components.
  Working Principle.
  Features.
  Working Model.
Prototype.
Actual Working Model.
Testing.
  Expected Results.
  Actual Results.
Maintenance.
  Interfacing SIM800 with Aurdino UNO.
  Sending Alerts to the Maintenance Department.
Conclusion.

## Slide 3: Problem Description
We all know that many accidents are being taking place at steep curves, bends and hilly areas and ruining out many lives of people and cattle.
We can prevent these accidents by proposing an idea on SENSORS.

## Slide 4: Proposed Idea
In this project with the help of Ultra-Sonic Sensors, Micro Controllers(Aurdino), and LED’s we can prevent accidents at steep curves and hilly areas.
By this project we can prevent many accidents irrespective of the vehicles having horns and lights.

## Slide 5: Components of Ultra-Sonic Sensor
Beam Transmitter
Beam Receiver
Voltage Supply( V cc )
Ground(GND)

## Slide 6: Working Principle
The major components of this project are Ultra- Sonic Sensors(HC-SR04), Micro Controllers (Aurdino UNO),Light Emitting Diode(LED) ,Transistors(NPN) and Batteries(9 Volts).
Working Of Ultra-Sonic Sensors:
The principle of Photo-Electric Sensor is based on reflection of beam which is being emitted by an inbuilt transmitter and this reflected beam is received by the inbuilt receiver whenever an obstacle has appeared.

## Slide 7
Initially when we provide power supply to this sensor, this gets activated and emits a beam of light to a certain range.
When this beam of light is caught by any obstacle the light gets reflected and this reflected light gets caught by the receiver present in the sensor.
This sensor consists of four pins. They are as follows:
1.Vcc(5 V) 3.Echo(INPUT pin)
2.Trig(Trigger) 4.GND(Ground)
Working Model

## Slide 8
  Power Supply :+5V DC
  Working Current: 15mA
  Effectual Angle: <15°
  Resolution : 0.3 cm
  Measuring Angle: 30 degree
  Trigger Input Pulse width: 10uS
  Dimension:45mmx20mmx15mm
Features

## Slide 9: Ultra-Sonic Sensor (HC-SR04) Working Principle
A high pulse of time period not less than 10 micro seconds is applied across Trigger(Trig) pin.
Sensor will generate a wave of 40KHz,we calculate the travel time by starting a timer with Echo pin as control.

## Slide 10: Diagrammatic Representation of Module

## Slide 11: Diagrammatic Representation of Module

## Slide 12: Diagrammatic Representation of Module

## Slide 13: Connecting Ultra-sonic Sensor(HC-SR04) with Micro-controller( Aurdino UNO )

## Slide 14: LED Connection with help of Transistor
e - Emitter
b - Base
c - Collector

## Slide 15: Software Used
Arduino

## Slide 16: Hardware Used
Parts | Quantity
Breadboards | 4
Sensors | 4
LED lights | 8
Connecting wires | Required no:
Arduino | 1
Batteries | 2
Metal Plates | 2
Power Supply | 5v

## Slide 17: Outlook of Our Project

## Slide 18: Outlook of Our Project How It Will Be

## Slide 19: Test Cases
Here we have done different test cases such as
Test Case | Expected Result | Pass/fail
Passing an object in front of a sensor1 | The led should glow | pass
Passing an object in front of a sensor2 | The led should get off | Pass
Passing an object in front of a sensor1 | The count should increment | Pass
Passing an object in front of a sensor2 | The count should decrement | Pass
Place an object in front of a sensor1 | Count should increment only once | Pass
Place an object in front of a sensor2 | Count should increment only once | Pass

## Slide 20: Test Case

## Slide 21: Test Case

## Slide 22
Sample Test Case What Should Happen

## Slide 23: Sample Test Case Practically

## Slide 24
Sample Test Case

## Slide 25
Maintenance
Interfacing SIM800 With Aurdino UNO

## Slide 26: Sending Alerts to Maintenance Department
via
SIM800 Module

## Slide 27: Conclusion
By this we conclude that by implementing
our project , accidents near the steep curves
especially in ghat roads, villages, forests etc
This is more helpful at nights.
This is cost effective, easy to install and maintain.

## Slide 28
THANK YOU
Any Questions..?